Part I Combinational Logic and Arithmetic

- Arithmetic
  - Padding 0’s to make some larger-bit number (e.g. 8-bit), before taking 2’s complement
  - Overflow happens when carry out bit does not match carry in for the highest order
- Combinational logic
  - properties of the XOR (important properties to know are XOR w. 0, XOR w. 1 property)
  - implementations with only NAND and NOR gates – saving time if it comes up
  - NAND is invert-OR or AND-invert logic
  - NOR uses invert-AND or OR-invert logic (NOR is the dual of NAND)
  - Constructing the other gates with NANDs and NORs
    - AND...with NAND (AND-invert logic) an inverter placed after NAND is AND
    - OR ...with NAND (invert-OR logic) an inverter placed in front of NAND is OR
    - OR...with NOR (OR-invert logic) an inverter placed after NOR is OR
    - AND...with NOR (invert-AND logic) an inverter placed before NOR is AND
    - NOT gates (single line inverters) are already considered NAND or NOR gates
- Combinational design
  - decoders nothing more than a bunch of two level AND-OR logic implemented with wiring to form minterms.
  - decoders can form a boolean function from input signals and combinational logic
  - Properties of decoders:
    - n inputs, and up to 2^n outputs (assuming all minterms are needed)
    - if properly working produces only a 1 (or high Voltage signal) on 1 output line the rest low Voltage signal.
  - multiplexers are built similarly to a decoder but with an additional layer of OR logic that sends one “input signal” to the single mux output (1 mux = 1 output)
  - internally the mux decodes selectors and determines which input lines to route or direct to output.
  - Properties of MUXes:
    - 1 output, n selectors and 2^n input lines
    - MUXes can be tricky in terms of variable assignment...which variables to assign where...what to do when more variables than selector lines for example!!?
  - Properties of adders/subtractors:
    - cascading n full adders within a combined circuit using “selector” line and XOR gates that pair directly with a bit string from the input, but also carry-in
    - when the selector is 0 the adder/subtr circuit is just a regular binary adder
    - for subtraction (selector = 1) the XOR complement with 1 is the 1’s complement and a carry-in 1 is added (carry in propagates!) that yields 2’s complement = 1’s + 1

Notes:
    - To make the logic work with these new components, K-maps, truth tables, are needed to design the logic...think of the decoder/mux as offering the physical implementation of making the circuits “easier” then in that way.
    - Both MUXes and decoders can be chained together to expand their uses into other larger ones. Probably not on the test, but it was on the homework...enable input lines help to do this.
    - The logic of a basic (half adder) is S and C, where S = a XOR b, and C = ab, for a full adder that adds 3 bits, it gets wild hence just knowing how it works is enough not why it does what it does.

Part II Sequential circuits

More Content to Review for midterm 2:
17-Oct	Sequential Circuits	Assign 5	5.1-5.4
24-Oct	Sequential Circuits	Assign 6	5.5
	Sequential Circuits	Slides
7-Nov	Sequential Circuit Design	Assign. 7	5.7-5.8

- Sequential circuits
  - Latches/Storage/D-type flip flop offer feedback of output into the inputs for state dependent on inputs as well as present state of the circuit (determining future state)
  - State tables
  - State diagrams
  - Moore vs. Mealy
  - Sequential circuit analysis
  - Other midterm review topics