Boolean Algebra
    - A truth table is helpful for describing the relations among variables and operators
    - A boolean function can be algebraically derived from a truth table by forming minterms and maxterms.
    - The minterm whose sum defines the Boolean function are those that give the 1’s of the function in the truth table.
    - Also the function complement is given by 0’s in such a table.
    - Form the function by adding or using the “or” operation of all those terms where F = 1.
    - A function’s complement is obtained from interchanging all 0’s for 1’s and 1’s for 0’s in the value of F.
    - The ways of complementing a function are with DeMorgan’s law, which is also possible by taking the dual and complementing each literal.
    - Look for some better proof or definition of the Boolean function complement. But for now in regards to conversion between canonical forms this is going to have to be enough.
    - To read a function complement from a truth table is to use the same process of “or” on all terms with value of 0 instead. (Now demorgan’s law to take complement of that!)
    - The maxterm can also be read directly from the truth table by taking the “and” of all terms whose standard products are equal to 1, in other words whose minterms are 0 and maxterms 1.
    - The canonical form is the sum of minterms or product of maxterms only – meaning basically unsimplified but accurate nonetheless.
    - Since 2n minterms/maxterms exist and for defining functions each one can be either 0 or 1 therefore actually 22n possible functions that can be formed with n variables.
    - Examples
Other Common relationships in boolean algebra
XOR => X XOR Y = XY’ + X’Y
Special case, X XOR X’ = 1, which is true because X + X’ = 1

Mapping and Gate-Level Minimization
    - With 4 variable map look at the difficult to spot edges on all 4 corners, as well.
    - The use of Gray code here is to make 1 bit changes moving up, down, left or right (diagonally...would actually constitute a 2 bit change)
    - K-Map is used to convert the algebra into a map/grid and simplify these functions
    - From the map the results are more obvious (and depend on the # of vars, 2, 3 and 4)
    - General reminders about using the K-maps:
    - The purpose is to show functions in their simplest form, which generally occurs from combining more squares to yields a simpler term and less literals in a term (both good)!
    - When working with the process begin with the largest count of legal adjacent boxes and work down also making use of overlapping squares and counting more than once is ok!!
    - Essential prime implicants are a way of dealing with the function via several K-maps of the same size with all terms accounted for in either one of the maps (essential/other)
    - To enter a function expressed in product of sums form into a map use the complement of the function to find the squares that are to marked by 0’s (double check this)
    - F = x’z + xz’ is the exclusive-or relationship
    - F = xz + x’z’ is the equivalence relationship resulting from (x’z+xz’)’
    - Two-level gate circuits come in several shapes and forms, including the AND-OR (sum of products), the OR-AND (product of sums), then also NOR-AND (??), and either AND-NOR and NOR-NOR (check facts here).
    - In sum of products implementation by a group of AND gates, connected to a single OR gate.
    - In product of sum implementation a group of OR gates precedes a single AND gate.
    - If the problem says the inputs are available directly and with their complements, so that inverters are not needed, or directly only inverters are needed.
    - A two level NAND gate circuit implements a sum-of-minterms function and is equivalent to a two-level AND-OR circuit.
    - Going from AND-OR logic to NAND requires checks on the overall polarity of circuit to see if it is switched in which case an extra inverter may be required at the end, or even for a single input signal. Alternatively begin with a simplified sum of products form (standard form), and then:
      - 1) make a NAND gate for each term with more than 1 literal, for the first level,
      - 2) make a NAND or inverted OR gate with inputs from prior level.
      - 3) Check if the single term literals may need to be complemented/inverted.
  - Example
    - functions of higher levels (more than 2 levels of gates)
      1. if implemented right away:
      1. F = A(CD+B)+BC’	has 4 levels of gates
      2. F = (AB’+A’B)(C+D’)	has 3 levels of gates … see why?