Chapter 5 Synchronous Sequential Logic (Shift to Part II of class)
5.1 Introduction
- Devices that depend on storage of data in memory elements
- Operation and control of digital systems
- Prior circuits (combinational) where output was depends on immediate inputs
- Now in Sequential circuits they have memory can store and retrieve

5.2 Synchronous sequential circuits (clocked)
- Sequential circuits are specified by a time sequence of inputs, outputs and internal states (synchronous and asynchronous)
- Synchronous - outputs derived from inputs at discrete instants of time, e.g. clocked sequential circuit, is synchronized to occurrence of clock pulses
- Asynchronous - outputs depend on signals time and order in which they change
- Synchronous sequential circuits, e.g. with clock pulses, manage discrete time and transition at predetermined intervals. (very stable systems in general)
- Clock pulses determine when computational activity will occur within the circuit, and other signals (external inputs and otherwise) determine what changes will take place affecting the storage elements and the outputs.
- In a clocked circuit the Internal state is stored in the memory elements called flip-flops
- What is a Flip flop?
  - Flip flops provide memory or storage of a single bit, and appear very often
  - In a stable state its output is either a 0 or 1 and it can only be changed at predetermined times based on the clock pulse cycle
    - The role of the clock pulse is just to close the switch and make the circuit complete. And New values when stored are updated at each clock cycle (hold time applies)
  - A 64-bit word would require 64 flip flops, and sequential circuits can use as many flip flops needed too.
  - The speed of any combinational logic circuit feeding the input of the flip flop is critical and must be completed and reached a stable value before the next clock pulse.
- (The asynchronous storage element is a time-delay device)
- Latches
  - Unlike a flip-flop which is edge sensitive, the latches that make up the building block of the flip-flop is level sensitive
    - The latches do not change each clock cycle
  - Wired as two cross-coupled NOR gates or two cross-coupled NAND gates:
  - SR Latches, in implementation using NOR gates the setting of both inputs at 1 is forbidden, otherwise S=1 sets, and R=1 resets and moving back to 0 has no effect at all
  - In the case of the S’R’ latch it is the NAND gate implementation since 0 0 is forbidden
  - Another further wiring is with a control input (enable) using two more NAND gates for S and R connected to Enable. By setting enable to 0 it is in effect telling the latch to stay at the same value, similar to moving to a No change state without it.
  - SR latch is the foundation to construct other useful latches and flip-flops.
  - Transparent latch (D-latch) fixes the problem of the indeterminate state of the SR latch, it does this by inverting the line (D input) so that at most either the Set or Reset side of the latch is active, not both. When the enable input gets asserted the D input is transferred to the Q output. Therefore it stores data, and is the fundamental building block for creating a D flip-flop.
5.4 Storage Elements: Flip-Flops
- More flip-flop terminology
  - Change in control input of a latch or flip-flop switches its state (it is triggered)
  - A clock pulse applied to a D-latch at the control input (enable input) is the design for an edge-triggered flip flop (rising edge or falling edge).
- Edge-triggered D flip-flops
- T flip-flops
- JK flip-flops
- State equations
- State tables
- State diagrams
- Mealy and Moore Models of he Finite State Machines
- State reduction (to another equivalent circuit)
- State assignment (pg 320-321)
- State diagram for T flip-flop pg 328 of a three-bit binary acounter