(in class notes)
Midterm review
- Design combinational circuits including decoders/multiplexers
- Use adders, adder/subtractors
- Binary arithmetic...Adding and subtracting binary numbers using 2’s complement
- Develop logic, state table, diagram from a set of input equations (and from a problem description).

F1 = AB + A’B’C = Em(1,6,7)
F2 = AB + A’BC’ = Em(2,6,7)
F3 = AB + AB’C’ = Em(4,6,7)

Decoder needs to take 3 select inputs, and therefore 2^3 outputs.
Convert fuctions into minterms and form a truth table with them.

Drawing the decoder
Highest order bit (of the input signals) has to go on top.
The combinational logic is always on the right side of the device (decoder)

F = AB + A’B’C + A’BC’
(Multiplexers can only implement one function each...if > 1 function then a multiplexer for each function)
Truth table in pairs of two, and then write the function as a function of the lowest order bit (only bit that changes in each grouping). In addition to C and C’ F may also be equal to 0 or 1 when rewritten as a function of the lowest order bit.
Need a mux with 2 select inputs that selects 4 input lines according to the rewritten functions.
Don’t assume the complement is available, and 0 and 1 is always available.

Functionality of a Full Adder
Truth table with CarryIn, A, B, CarryOut and Sum….Just add the bits on the left of the truth table, and plac in the correct column of Sum lower bit and Carry higher bit.
Or implementing (not circuitry, but concept of it...combinational circuit)….stringing Full Adders together to make a larger adder/subtractor.
Adder/subtractor only works with the 2’s complement system. Using XOR gates for one of the input signals to switch between addition and subtraction. For addition just add bit strings. For subtraction add the 2’s complement to perform subtraction. (Drop carry values).
XOR – x XOR y, if x is a 0 then output is y, if x is a 1 the output is y’