CS42 Supplementary Notes about Computer Architecture

Source: 61C at Berkeley lectures

Textbooks used:
Data Centers as Computers
C Programming K&R
Also a typical computer architecture textbook.

Week 1 (Intro)
Goals:
- Creating or designing a working computer that makes use of real physics
  - Abstraction in the representation is useful, e.g. not always important to draw, represent or refer to the lowest level of what is happening….e.g. a logic gate or block could be (and is made of transistors) but what does that help with the design problem?)
- Performance measurement and improvement (engineering discipline)
  - One source of increased performance (high performance computing) is Parallelism
- Applying all of the computer architecture to big data
- Learning the inner workings of a process/CPU from both hardware and software perspective.
  - Hardware: Learning how programmable logic gates work to compute. A memory hierarchy (principle of locality). Instruction sets on a processor.
  - Software: C allows some better access to lower level system of hardware than languages like Python or Java, etc. In Computer Architecture C programming is useful for bringing to light the key hardware features. And also C Programming will be used to access the hardware parallelism for performance.

Computer Architecture Ideas
- Gordon Moore (Moore’s law)...Intel started with memory chips and then moved to making processors. Predicted the cost of making chips 2X transistors / chip every 2 years. Cost per transistor. How many transistors can fit on a die. The shrinking size and lowering cost has caused the industry to grow a lot! This law is as much about cost as size of transistor and it is basically over.
- Computers are mostly memory that is used to manage data. Bigger memory = bigger latency. How far away is the data? Most of the memory is off chip (>100 clock cycles), but for the Onchip cache and Onboard cache as well as the CPU’s registers, in the 1-4 nanosecond range. That’s a big difference. To disk is 10^6 ns (rotating disk). Tape archive is 10^9 ns.

Week 10 (or so)

Important hardware terms/concepts
Clock – a steady square wave that synchronizes system activity (also called CLK)
Setup Time – the time an input must be stable before the CLK wave rises
Hold Time – time an input must be stable after the CLK signal has risen
CLK-to-Q Delay – the time it takes output to change from the CLK signal rise
Flip-flop – one bit of state (complicated piece of hardware to design, built from gates/switches)
Register – multiple flip-flops working together

More basic hardware terms
Switches – switches are the inner pieces of circuitry, switches are “thrown” means they are properly doing their function and driving the larger gates, logic blocks, etc.

E.g. Dealing with the design issue of Propagation Delay
Multiple independent registers can help computer architecture to do things in parallel. This is done in pipelining (when introducing new registers in the middle) to increase the clock frequency, and provide higher bandwidth. The downside might be it results in more Latency (time it takes a signal to go from end to end), but parallel processing in effect.

E.g. Propagation time delay using Critical Path Analysis
Clock-to-Q 1 ns, Setup 1 ns, Hold 1 ns, AND delay 1 ns
A SL circuit with 1 register and 3 AND gates on its critical path is going to produce a clock frequency of 200 MHz. NOTE: Hold time does not effect the critical path analysis, but it is important for multiple registers capturing values in sequence to slow down (hold) the signal each later register.

Registers

Registers prevents the flow of the bits from being read too early, and holds the input until the next clock in. (Registers hold the input stable until the next clock cycle). Register input takes a snapshot of sorts of the input and waits until the clock cycle to send its output.

The Clock on the system uses Flip Flops. Clocking “in” means capturing the values on the circuit and afterwards bits can once again be changed. On a larger scale the entire system can be built with CL and registers. (Combinational Logic).

Flip flops
Registers are made up of flip flops?
Flip flops – only changes on the clock signal rise (edge trigger).
All the clock signals are wired together throughout the system.

Building a computer design requires

Multiplexer
Arithmetic and Logic Unit
Adder and Subtractor

A Mux (multiplexer) is a selector which directs the inputs to output. Again, the Mux selects one of the signals according to the select signal and propagates it to the output regardless of the value of the other input.
A 2-to-1 needs only 1 selector bit. N-bit wide mux can be made of N instances of a 1-bit-wide mux.

2-to-1 mux has 3 inputs and 1 output. 8 rows in a truth table.
s a b	c	c = combinational logic output
000	0
001	0
010	1
011	1
100	0
101	1
110	0
111	1

c	=	s’ab’ + s’ab + sa’b + sab
 =	s’(ab’ + ab) + s(a’b + ab)
 =	s’(a(b’ + b)) + s((a’ + a)b)
=	s’(a(1)+s((1)b)
=	s’a + sb

(Insert circuit diagram)

4-to-1 multiplex (6 inputs, truth table of 64 rows!!)
e = s1’s0’a + s1’s0b + s1s0’c + s1s0d
- Can be built with two 2 input muxes in cascade
- The other way to build is to make the circuit with a single 4 input selector
- Extremely common components (registers and muxers)

Arithmetic and Logic Unit
- The heart of the CPU where arithmetic and logic takes place
- Addition and subtraction
- AND and OR
- Like a mux the ALU involves two selects that drive a mux
- The simple ALU will have three units inside (combinational) one for add/subtract, one for AND and one for OR. Each time the ALU processes the signal it will calculate all 3 for the inputs, and the selector will determine which of the signals to use for the given purpose.
- The only drawback to this parallel-ism is the power drawn to do the work, but in a simple enough ALU it could be more power costly to do anything to try and stop the parallel computations.
- Solid state parts means these parts do not wear down/wear out over time (very slowly).